## Slide 1: Advanced pcb lab
Marvin the hackbot

## Slide 2: Secondary micro controller
Purpose
  Generating motor driver pwm
  Controlling motordriver
  Controlling hc-sr04
  sending data to the main microcontroller

## Slide 5: Main micro controller
Purpose
  Generating data for esp8266
  Controlling levelshifter
  Controlling hc-sr04
  receiving data from the secondary controller

## Slide 8: Why to microcontrollers?
Taking load of the controller(interrupt wise)
Relatively more i/o available

## Slide 9: Encoders
Rover chassis=> quadrature encoders
Number of sensors can be used
  Optical(IR pair) => whit black and withe surfaces
  Magnetical(hal sensor) => magnet on a shaft
Pulses 90degrees out of phase

## Slide 11: ESP8266
Cheap wifi module
with onboard System On chip
Communicating protocol=> AT commands via serial port
No components under the antenna!
3.3V ONLY!!! No 5V tolerant I/O

## Slide 13: Level shifter
Converts signal other voltage level
  For example 3.3V to 5V
TXB0108 uses 2 voltage supply’s
  Vcca => 1.2V to 3.6V
  Vccb =>1.65V to 5.5V
Needs to be used because of the esp8266
Level shifter needs to be enabled via OE pin

## Slide 15: Motor driver
TB6612FNG
  Integrated H-bridge with integrated control circuit’
    No need to worry about short circuiting the internal mosfets
Iout 1.2A Max with peak current up to 3.2A

## Slide 17: Rc reciever

## Slide 19: Ultrasonic distance sensor

## Slide 21: Power supply
Uses ldo’s
  Low dropout voltage
Used to generate 5V and 3.3V for control electronics