## Slide 1: Advanced pcb lab
Marvin the hackbut
By Ben De Lathouwer

## Slide 2: Agenda
Designing a PCB

## Slide 3: Goal of advanced pcb lab

## Slide 4: Main micro controller
Purpose
  Generating data for esp8266
  Controlling levelshifter
  Controlling hc-sr04
  receiving data from the secondary controller

## Slide 5: Main micro controller V2

## Slide 6: Main micro controller V3

## Slide 7: Secondary micro controller
Purpose
  Generating motor driver pwm
  Controlling motordriver
  Controlling hc-sr04
  sending data to the main microcontroller

## Slide 8: Secondary micro controller V2

## Slide 9: Secondary micro controller V3

## Slide 10: Why to microcontrollers?
Taking load of the controller(interrupt wise)
Relatively more i/o available

## Slide 11: Encoders
Rover chassis=> quadrature encoders
Number of sensors can be used
  Optical(IR pair) => whit black and withe surfaces
  Magnetical(hal sensor) => magnet on a shaft
Pulses 90degrees out of phase

## Slide 12: Encoders V2 & V3

## Slide 13: ESP8266
Cheap wifi module (6 euro’s)
with onboard System On chip
Communicating protocol=> AT commands via serial port
No components under the antenna!
3.3V ONLY!!! No 5V tolerant I/O

## Slide 14: ESP8266 V2 & V3

## Slide 15: Level shifter
Converts signal other voltage level
  For example 3.3V to 5V
TXB0108 uses 2 voltage supply’s
  Vcca => 1.2V to 3.6V
  Vccb =>1.65V to 5.5V
Needs to be used because of the esp8266
Level shifter needs to be enabled via OE pin

## Slide 16: Level shifter V2 & V3

## Slide 17: Motor driver
Using h-bridge
TB6612FNG
  Integrated H-bridge with integrated control circuit’
    No need to worry about short circuiting the internal mosfets
Iout 1.2A Max with peak current up to 3.2A

## Slide 18: Motor driver V2 & V3

## Slide 19: Rc reciever
Standart modelling rc receiver
Servo output
Wirles communication
Gets transformd into
Pwm signal

## Slide 20: Rc receiver V2 & V3

## Slide 21: Ultrasonic distance sensor
Measurement using sound
4 pins
  Gnd, vcc triger input and echo output
Echo puls with proportional to distance
  distance = high level time * velocity (340M/S) / 2
    High level= duration of puls with(milli or micro seconds)
    velocity = 340M/S

## Slide 22: Ultrasonic distance sensor
Ranging distance = 4cm to 4meters
Detection angle is 15 degrees

## Slide 23: Theoretical signals

## Slide 24: Trigger puls

## Slide 25: Echo puls minimum distance

## Slide 26: Echo puls max distance

## Slide 27: Ultrasonic distance sensor V2 & V3

## Slide 28: Power supply
Uses ldo’s
  Low dropout voltage
Used to generate 5V and 3.3V for control electronics

## Slide 29: Power supply V2

## Slide 30: Power supply V3

## Slide 31: Improvments for MK4 pcb

## Slide 32: What did I learn ?
Circuit design
Think first then design
  First reading the datasheet
  Then draw footprints etc.
High current design
Using Altium
Notes: used the wrong interrupt source

## Slide 33: Questions?